pipeVue Layout and Cylinder Scripts

This document describes the contents and forms of Layout Scripts and Cylinder Scripts as used with the pipeVue program. Layout Scripts tell pipeVue the locations of posts it should generate. Cylinder Scripts tell it where to draw cylinders between posts.

Note, the layout and cylinders scripts that pipeVue uses are selected in accord with command-line parameter values. If the first parameter is a valid integer k (or blank, which means k=0), then pipeVue uses the kth built-in script set. Each built-in script set contains a layout script and a cylinders script. Otherwise, the first parameter should be the name of a file containing such scripts. In a script file, lines of form `=xd` are section separator lines, where x is L or C for layoutscript or cylinder script, and d is don’t-care text. Lines before the first separator line are comment lines. For examples, see `eg-pentagon-script`.

Layout Scripts
A layout script consists of a series of entries separated by semicolons. There are several kinds of entries: Polygon; Rectangle grid; Triangle grid; Line of points; Collection of x,y,z points; and Base point. Each entry begins with a letter, B, C, L, P, R, or T to designate its type. Note: pipeVue applies a scale factor to all the location data (coordinates and radii) when producing output. The scale factor is given by command line parameter SF and its default value is 100.

Each base point entry has three parameters: x,y,z, which specify an anchor point, or base point, denoted BP, for use when treating C, L, P, R, or T entries. By default BP is (0,0,0). Example: "B 5.7, 2.2, 1.5;" sets BP to (5.7, 2.2, 1.5).

Each polygon entry has three parameters, n, r, a0. n is corner count; r is radius from BP to corners; and a0 is the angle from BP to the first corner, in degrees CCW from the positive x axis. Post numbers increase going CCW. For example, "P5,1,0;" denotes a pentagon of posts with radius 1 (before scaling). As another example, "P12, 3.37, 11.5;" denotes a 12-gon of radius 3.37, rotated 11.5˚ CCW.

Each rectangle grid entry has four parameters, r, c, dx, dy. Integers r and c are the number of rows and columns to generate; decimals dx and dy are the width and height between columns and rows. Example: "R 5, 7, 2.2, 1.5;" makes a rectangular grid of posts, with five rows and seven columns, with columns spaced 2.2 apart and rows spaced 1.5 apart (before scaling). Note: for rectangle and triangle grids, points in the same row have consecutive numbers. A grid’s first point is at BP, the second is at BP+(dx,0,0), and so forth.

Each triangle grid entry has four parameters, r, c, dx, dy, where r and c are the number of rows and columns to generate and dx, dy are width and height between columns and rows. Even-numbered rows have one fewer points than do odd-numbered rows. Thus, row 0 has r posts in it, row 1 has r+1, row 2 has r, and so forth, giving rc+(r//2) points in all. Even-numbered rows are offset by dx/2 relative to odd-numbered rows. Example: "T5, 5, 1, 0.866" produces 27 posts (27=5·5+5//2) that are on a grid of equilateral triangles with unit side.

Each line of points entry has four parameters: n, dx, dy, dz. n is the number of points in the line. The first point in the line is at BP and (dx,dy,dz) is the x,y,z step between consecutive points. Example: If BP is (2, -2, .2), then `L4 3,1,.01;` makes posts at (2, -2, 0.2); (5, -1, 0.21); (8, 0, 0.22); (11, 1, 0.23).

Each collection of points entry has a list of x,y,z values, and a semicolon terminator. For each x,y,z value, a post is produced at BP+(x,y,z). Example: If BP is (0.1, 0.2, 0.3), then `C 1,1,1, 4,4,1, 5,6,7 7,11,13;` makes posts at (1.1, 1.2, 1.3); (4.1, 4.2, 1.3); (5.1, 6.2, 7.3); and (7.1, 11.2, 13.3), in order.

Cylinder Scripts
A Cylinder Script is a string of entries, each specifying one cylinder. Each entry is composed of optional <color>, <diam>, <post>, and <level> elements, and is terminated by a semicolon, as explained below. Here is an example script which draws four thin differently-colored horizontal cylinders at different levels: "qG 0a1a; R2bb3; C4cc5; M6dd7;". In this example, "R2bb3;" specifies a red cylinder of thickness q from level b of post 2 to level b of post 3.

 <color> is one of G, Y, R, B, C, or M for green, yellow, red, blue, cyan, magenta.

<diam> is p or q, where (by default) p is thick, q is thin.

Each entry allows optional <post> numbers and optional <level> codes, that is, a letter (a-e) for a level on a post. Level a is low, e is high, and others are spread proportionally between. For example, "14b26c;" specifies a cylinder from level b on post 14 to level c on post 26, using whatever color and diameter were previously specified. As another example, "7e;" specifies a cylinder to level e on post 7, from the most recently given post and level, using previously specified color and diameter.

The semicolon after an entry is required punctuation. Whenever a semicolon appears, a cylinder is produced, using the most recently given post numbers and levels, whatever they are, and the most recent color and diameter.

Most elements are optional within each entry, and elements not given remain as previously specified. For example, the specification "Ccc0,1;2;3;4;" draws four cyan-colored cylinders, in a chain from post 0 to 1 to 2 to 3 to 4, with all cylinder-ends at level c. As another example, "qCab0,1;c;d;e;" draws four thin cylinders between posts 0 and 1, going from 0a to 1b; from 0b to 1c; from 0c to 1d; and from 0d to 1e.

Initial defaults for color, thickness, level, and post are G, p, a, 0. White space and characters not listed above are ignored, except that they delimit post numbers. For example, the entries quoted in the following set are equivalent: { "Gp0a1e;" "pG0ae1;" "ae0Gp1;" }