pipeVue Layout and Cylinder Scripts

This document describes Layout Scripts and Cylinder Scripts as used with the pipeVue program. Layout Scripts tell pipeVue the locations of posts it should generate. Cylinder Scripts tell it where to draw cylinders between posts.

Note, the layout and cylinders scripts that pipeVue uses typically are read from a file. To specify a file, use a command line parameter in the form"f=filename" where filename is a script file name. (pipeVue uses a simple built-in script when no file is specified.) In a script file, lines starting with one of `=P`, `=L`, or `=C` mark the beginnings of parameter, layout, or cylinder text. Other lines starting with `=`, blank lines, and lines before the first marker line are comment lines. For examples, see files like eg-cap-5, eg-cap-6, eg-fatpost-redstar, eg-pentagon-script, eg-several-kinds, and eg-two-rings. Note, parameters are given new values by entries like "pDiam=.1" in the =P section of a script file. Each entry should be separated from other entries by white space, and should contain no white space itself.

[Initially, parameter values are set by python statements in the the program. Next, parameter values are set per command-line options, each of which is in a "var=value" form. If one of the command-line options is f=filename, parameter and script texts are read from file, and parameter values are set per those texts. Parameter values are again set per command-line options before posts and cylinders are generated. If any parameter is specified in both places (command and file), its command-line value prevails over its file value.]

Layout Scripts
A layout script consists of a series of entries separated by semicolons. There are several kinds of entries: Base point; Collection of points; Line of points; Polygon; Rectangle grid; and Triangle grid. Each entry begins with a letter, B, C, L, P, R, or T to designate its type. Note: pipeVue applies a scale factor to all the location data (coordinates and radii) when producing output. The scale factor is given by parameter SF and its default value is 100.

Each base point entry has three parameters: x,y,z, which specify an anchor point, or base point, denoted BP, for use when treating C, L, P, R, or T entries. By default BP is (0,0,0). Example: "B 5.7, 2.2, 1.5;" sets BP to (5.7, 2.2, 1.5). Files eg-cap-5, eg-cap-6, and eg-several-kinds move the base point before making polygons, grids, and lines of points.

Each polygon entry has three parameters, n, r, a0. n is corner count; r is radius from BP to corners; and a0 is the angle from BP to the first corner, in degrees CCW from the positive x axis. Post numbers increase going CCW. For example, "P5,1,0;" denotes a pentagon of posts with radius 1 (before scaling). As another example, "P12, 3.37, 11.5;" denotes a 12-gon of radius 3.37, rotated 11.5˚ CCW.

Each rectangle grid entry has four parameters, r, c, dx, dy. Integers r and c are the number of rows and columns to generate; decimals dx and dy are the width and height between columns and rows. Example: "R 5, 7, 2.2, 1.5;" makes a rectangular grid of posts, with five rows and seven columns, with columns spaced 2.2 apart and rows spaced 1.5 apart (before scaling). Note: for rectangle and triangle grids, points in the same row have consecutive numbers. A grid’s first point, in row 0, is at BP+(0,0,0), the second is at BP+(dx,0,0), and so forth. Row 1 starts at BP+(0,dy,0), then BP+(dx,dy,0) for a rectangle grid, or at BP+(-dx/2,dy,0) , then BP+(dx/2,dy,0) for a triangle grid. Row 2 starts at BP+(0,2·dy,0), then BP+(dx,2·dy,0), then BP+(2·dx,2·dy,0), etc.

Each triangle grid entry has four parameters, r, c, dx, dy, where r and c are the number of rows and columns to generate and dx, dy are width and height between columns and rows. Even-numbered rows have one fewer points than do odd-numbered rows. Thus, row 0 has r posts in it, row 1 has r+1, row 2 has r, and so forth, giving rc+(r//2) points in all. Example: "T5, 5, 1, 0.866" produces 27 posts (27=5·5+5//2) that are on a grid of equilateral triangles with unit side. As noted in the previous paragraph, even-numbered rows are offset by dx/2 relative to odd-numbered rows.

Each line of points entry has four parameters: n, dx, dy, dz. n is the number of points in the line. The first point in the line is at BP and (dx,dy,dz) is the x,y,z step between consecutive points. Example: If BP is (2, -2, .2), then `L4 3,1,.01;` makes posts at (2, -2, 0.2); (5, -1, 0.21); (8, 0, 0.22); (11, 1, 0.23).

Each collection of points entry has a list of x,y,z values, and a semicolon terminator. For each x,y,z value, a post is produced at BP+(x,y,z). Example: If BP is (0.1, 0.2, 0.3), then `C 1,1,1, 4,4,1, 5,6,7 7,11,13;` makes posts at (1.1, 1.2, 1.3); (4.1, 4.2, 1.3); (5.1, 6.2, 7.3); and (7.1, 11.2, 13.3), in order.

Cylinder Scripts
A Cylinder Script is a string of entries, each specifying one cylinder. Each entry is composed of optional <color>, <diam>, <post>, and <level> elements, and is completed by a semicolon, as explained below. Here is an example script which draws four thin differently-colored horizontal cylinders at different levels: "qG 0a1a; R2bb3; C4cc5; M6dd7;". In this example, "R2bb3;" specifies a red cylinder of thickness q from level b of post 2 to level b of post 3.

 <color> is one of G, Y, R, B, C, M, or W for green, yellow, red, blue, cyan, magenta, white.

<diam> is a letter, p, q, r, … w. By default, pDiam=0.06 and qDiam=0.02. The thicknesses of r, s,...w scale geometrically according to parameter dRatio, which is sqrt(2) by default. Thus, r is about 1.41·q, s is 2·q, and so forth. File eg-two-rings illustrates changing dRatio to a smaller value to get more-gradual increase in pipe size.

Each cylinder entry allows optional <post> numbers and optional <level> codes, that is, a letter (a-e) for a level on a post. Level a is low, e is high, and others are spread proportionally between. For example, "14b26c;" specifies a cylinder from level b on post 14 to level c on post 26, using whatever color and diameter were previously specified. As another example, "7e;" specifies a cylinder to level e on post 7, from the most recently given post and level, using previously specified color and diameter.

The semicolon after a cylinders entry is required punctuation. When a semicolon appears, a cylinder is produced. Ordinarily, the cylinder uses the most recent post numbers, levels, color, and diameter. But if the entry just concluded had no post numbers in it, a special action occurs: the latest post numbers are each incremented by 1 before the cylinder is drawn. This allows writing "1,11;;;;;" instead of "1,11; 2,12; 3,13; 4,14; 5,15;", or allows writing "1,2;;;;1;" instead of "1,2;3;4;5;1;", which in turn is equivalent to "1,2; 2,3; 3,4; 4,5; 5,1;".

A special character "/" also is allowed in cylinders entries. The slash0 is shorthand for swapping the two most recent levels. This allows writing, for example, "ae1,2;/;/;/;/1;" instead of "ae1,2;a3;e4;a5;e1;".

Most elements are optional within each entry, and elements not given remain as previously specified. For example, the specification "Ccc0,1;2;3;4;" draws four cyan-colored cylinders, in a chain from post 0 to 1 to 2 to 3 to 4, with all cylinder-ends at level c. As another example, "qCab0,1;c;d;e;" draws four thin cylinders between posts 0 and 1, going from 0a to 1b; from 0b to 1c; from 0c to 1d; and from 0d to 1e.

Initial defaults for color, thickness, level, and post are G, p, a, 0. White space and characters not listed above are ignored, except that they delimit post numbers. For example, the entries quoted in the following set are equivalent: { "Gp0a1e;" "pG0ae1;" "ae0Gp1;" }